## Slide 1
Progress Updates
Detail Appendix

## Slide 2
编号 | 任务项 | 时间占比 | 优先级 | Mar | Apr | 
 |  |  |  | CW13(03/28) | CW14(04/04) | CW15 (04/11)
#1 | PULP FPGA Demo | 30% | 2nd | 1）基本概念梳理 2）完成demo-1 | 1）完成demo-2 2）完成demo-3 | 1）完成demo-4 2）总结文档
#2 | 芯片设计流程培训 | 40% | 1st | 1）静态时序分析基础课件 2）逻辑综合课件 | 1）时钟树综合课件 2）功耗/IR/EM课件 | 1）上机脚本梳理 2）实例图片插入
未来三周计划
#1 FPGA Demo的进度没有按预期进行，预计delay 1周；
原因是Linux系统/RISCV Toolchain/QuestaSim/Vivado的安装破解花了一周时间
#2 的进度目前可控，预计4月12号前 close
100%
50%
50%

## Slide 3
Progress Updates
Detail Appendix

## Slide 4: PULPino
Single 32bit RISC-V core MCU
riscy
zero-riscy
2 stage
in order
4 stage
in order
Taped out with UMC 65nm Jan-2016
RTL simulation as well FPGA prototype

## Slide 5: PULP Basics RISC-V compatible cores written in SystemVerilog
Overview
Silicon Proven designs !
Source : https://pulp-platform.org//implementation.html
Source : https://pulp-platform.org//

## Slide 6: FPGA Board Basics
Overview
source: http://www.digilent.com.cn/products/product-arty-board-artix-7-fpga-development-board-for-makers-and-hobbyists.html

## Slide 7
Linux
PLUPino
GCC
Vivado
QuestaSim
Ubantu 18.04.1
10.4C
2018.03
Webpack

## Slide 8: Demo实验需要Linux环境
64bit的Linux安装32bit的程序 ！一系列安装Bug的起源！

## Slide 9: GCC Toolchain
https://github.com/pulp-platform/ri5cy_gnu_toolchain
make #Riscy
make RISCY_FPU=1 #Riscy_fpu (riscy with hardare floating point unit)
make ZERORISCY=1 #Zeroriscy
make MICRORISCY=1 #Microriscy
The resulting toolchains should be in the install directory
RISCV GCC toolchain, which has been extended to support the extensions of the Pulpino core
Build for supported cores
Introduction
Usage for supported cores
-march=IMXpulpv2 #Riscy
-march=IMFDXpulpv2 -mhard-float #Riscy_fpu
-march=IM #Zeroriscy
-march=I -m16r #Microriscy

## Slide 10: GCC Toolchain
缺少库/工具
  sudo apt-get install $name
  sudo apt-cache search $pattern
语法错误
  系统默认gcc-7 g++-7
  安装并切换到gcc-5 g++-5
谨慎删除库文件
  双系统卸载unbantu
稳定的网络环境

## Slide 11: GCC Toolchain
下载开源代码
  git clone $source_code_address -> ./update.py
下载编译器
  git clone $tool_chain_address
Commnet-1：
sudo apt-get install git
sudo apt-get install python-yaml
sudo apt-get install gawk
Commnet-2：
Be sure the internet connection is OK

## Slide 12: QuestaSim
QuestaSim其实就是Modelsim的扩展版，增加了System Verilog仿真的功能，除此之外，几乎没区别
  https://blog.csdn.net/k331922164/article/details/47988847
questasim作为modelsim的高级版，用着速度还是比modelsim爽很多，基本上所有操作指令都是和modelsim兼容的
  https://www.cnblogs.com/kingstacker/p/11431232.html
Modelsim也支持UVM 但不如Questa支持的好（比如assertion和覆盖率等方面）
Questa有64位模式 而Modelsim在64位OS上也只是32位模式
Questa可以同时启动多个波形窗口
Questa提供模拟数字混合仿真接口

## Slide 13: QuestaSim安装记录
QuestaSim 10.4c安装
  Linux版本安装包
    https://pan.baidu.com/s/1mg4GxHQ#list/path=%2F
  Crack包
    http://bbs.eetop.cn/thread-593767-1-1.html

## Slide 14: QuestaSim安装记录
lmgrd无法运行,原因是file lmgrd返回32bit
  apt-get install ia32-libs
  apt-get install lsb-core
ldd lmgrd查看缺少哪些库
  Find / -name $lib_name
  Apt-file search $lib_name => package_name

## Slide 15: Linux系统安装记录
安装Linux双系统
  下载镜像制作启动U盘
  DiskGenius腾出空余磁盘空间
  BIOS设置
  运行安装
  手动分区，将分区挂载到/ 和 /home
  关机（强制）重启

## Slide 16: 双系统卸载unbantu
https://blog.csdn.net/guikunchen/article/details/88077330?depth_1-utm_source=distribute.pc_relevant.none-task&utm_source=distribute.pc_relevant.none-task

## Slide 17: 地址空间
axi_node_intf_wrap
#( .NB_MASTER ( 3 ), .NB_SLAVE ( 3 ), .AXI_ADDR_WIDTH ( `AXI_ADDR_WIDTH ), .AXI_DATA_WIDTH ( `AXI_DATA_WIDTH ), .AXI_ID_WIDTH ( `AXI_ID_MASTER_WIDTH ), .AXI_USER_WIDTH ( `AXI_USER_WIDTH ) )
axi_interconnect_i
( .clk ( clk_int ), .rst_n ( rstn_int ), .test_en_i ( testmode_i ), .master ( slaves ), .slave ( masters ),
.start_addr_i ( { 32'h1A10_0000, 32'h0010_0000, 32'h0000_0000 } ),
.end_addr_i ( { 32'h1A11_FFFF, 32'h001F_FFFF, 32'h000F_FFFF } ) );
外设
1A10_0000
1A11_FFFF
DATA RAM
0010_0000
001F_FFFF
Boot ROM
0000_0000
000F_FFFF
实际代码确定Boot ROM起始地址是0x0000_8000
Instr RAM
0000_8000
top.sv

## Slide 18: Method1
D-Cache
I-Cache
Boot ROM
SPI Flash
D-Cache
I-Cache
SPI Flash
JTAG
SPI
Boot ROM
code
code
Method2